## Slide 1
Generously supported by:
CCAPP
The National Science Foundation
The Ohio Supercomputer Center
Evolving Antennas for Ultra-High Energy Neutrino Detection
Alex Machtay
Genetically Evolving NEuTrino teleScopes (GENETIS) Collaboration
APS Meeting April 19, 2020

## Slide 2
GENETIS
Using genetic algorithms to evolve detector designs
Members
  3 Professors
    Amy Connolly, The Ohio State University
    Carl Pfendner, Denison University
    Stephanie Wissel, Pennsylvania State University
  1 Research Scientist
    Kai Staats, North Western University
  1 Grad Student
  7 Undergrads
  Numerous former undergrad members

## Slide 3
Neutrino Radio Detection
Ultra-High Energy (UHE) neutrinos interacting with ice create particle cascades
These cascades emit Askaryan radiation
Experiments need to cover large areas to be able to detect events
Antennas are placed in holes drilled in the ice
[2]
[1]

## Slide 4
Can we use GAs to design better antennas?
Designed to mimic evolution
  Generate an initial population of possible solutions, or individuals
  Determine the fitness of individuals
  Select some individuals to be used to make the next generation
  Repeat until an ideal solution is approached!
Genetic Algorithms

## Slide 5
Antenna Response Targeted Evolution (AREA)
  Evolved ideal beam patterns for in ice neutrino detection
  Fitness function was the number of neutrino events that trigger the detector
Past Work
Cal Poly undegrads Corey Harris, Luke Letwin, and Jacob Trevithick
[3]

## Slide 6
Currently evolve bicone antennas with 3 genes
  Length, inner radius, and opening angle
        Genes for initial generation are generated from gaussian distributions
  Antenna beam patterns determined using an industry standard modeling software (XFdtd)
  Pass these beam patterns to neutrino detection simulation software (AraSim)
Evolving Antennas

## Slide 7
“The Loop”
Generate new population
Model individuals in XF to create beam patterns
Send beam patterns through AraSim
Calculate Fitness Score
Select individuals to create next generation
Total run time is ~3 hours per generation (for 10 individuals and 105 neutrinos)
XF | AraSim | Rest of Code | Total
2-3 hours | 1 hour | Negligible | 3 hours
[4]

## Slide 8
Fitness Function
Uses sensitivity of antenna to neutrino events as described by (VΩ)eff
  Neutrino energies are set to 1018 eV
Antennas are penalized for being too big
  Holes in ice are drilled with a 15 cm diameter
  Antennas bigger than are penalized to encourage the algorithm to make smaller antennas
Roulette Selection
  Higher fitness scores are more likely to be selected
[5]

## Slide 9
Only human interaction with the loop is at the start
Detector simulation
      Sped up by a factor of 2 since last year
      Parallelized in the loop (by a factor of 100)
        (OSU undergrad Alex Patton)
Developing a database of simulated antennas
      Eliminates the need to simulate the same antennas repeatedly
Efforts to Automate and improve speed

## Slide 10
Results
  Evolved 10 individuals for 10 generations using 105 neutrinos at Eν = 1018 eV
  Algorithm learns to create “fitter” antennas

## Slide 11
Keep evolving!
  Goal is hundreds of individuals and hundreds of generations
  Explore other types of algorithms
  Increase number of parameters
        Design asymmetric antennas
Build and test designs
  Center for Design and Manufacturing Excellence at OSU can help machine candidate antennas
  Deploy a prototype with Radio Neutrino Observatory in Greenland
Expand into other areas
  Use GAs to improve other aspects of experiments
Next Steps

## Slide 12
Bibliography
[1] LeCosPA Group, National Taiwan University
  https://lecospa.ntu.edu.tw/zh/experiment-zh/experiment-i-ultra-high-energy-neutrinos
[2] J. Alvarez-Muniz, ICRC 2017
  https://pos.sissa.it/301/1111/pdf
[3] “Optimization of Antennas in the Askaryan Radio Array Using Genetic Algorithms,” Corey Harris, Luke Letwin, Jacob Trevithick, 2018
[4] Askaryan Radio Array Info Page
  https://ara.wipac.wisc.edu/home
[5] Engineering Design Center, Newcastle University
  http://www.edc.ncl.ac.uk/highlight/rhjanuary2007g02.php/